## Slide 1
Center Avenue
Red River to 8th Street
Report on the
Planning & Preliminary Engineering Study
2019 Minnesota MPO Summer Workshop
August 28, 2018
Notes: Welcome & Introductions – Jon

## Slide 2
Project Location
Red River
8th Street
TO
Notes: Jon

## Slide 3: Needs Assessment
Poor Pavement Condition
High crash rates along the corridor
High volume of access points with limited left turn lanes
Lack of designated east-west bicycle facilities
Sight distance issues for some accesses
Roadway alignment shifts
Driving the Project’s Need
Center Ave & 4th Street
Notes: Jon

## Slide 4: Alternative Development
Developed 4 Base Alternatives
All Alternatives fix project need for existing pavement issues
Alternatives respond to needs assessment
4-Lane
WHAT IS RIGHT FOR CENTER AVENUE?
3-Lane
Notes: Peggy

## Slide 5: Alternative A
Mill & Overlay + 3-Lane Section +
Designated Bike Lanes
Notes: Peggy

## Slide 6: Alternative A
Alternative Improvements | Issued Addressed/Impacts
Mill & Overlay | Fixes pavement deficiencies
Roadway Section (3-Lanes) | Serves 2040 traffic volumes Eliminates alignment shifts Estimated corridor crash reduction of 24% Removes 4 Trees
Bike Facilities Across Bridge | Creates bike connection across bridge
Bike Facilities Along Center Ave | Provides on-street dedicated bicycle facilities
Transit | Removes transit pullout per request Maintains existing transit routes Creates vehicle delays when bus is stopped
Removal of 7th Street Signal | Allows coordination between signals Signal is not warranted
Pedestrians | Removes conflict between bikes and peds Improves ADA compliance
Access | Options to do nothing, relocate or close accesses
Parking | No Changes
Preliminary Cost | $975,000
Mill & Overlay + 3-Lane Section +
Designated Bike Lanes
Notes: Peggy

## Slide 7: Alternative B
Mill & Overlay + 3-Lane Section +
On-Street Parking/Wide Outside Lanes
Notes: Peggy

## Slide 8: Alternative B
Alternative Improvements | Issued Addressed/Impacts
Mill & Overlay | Fixes pavement deficiencies
Roadway Section (3-Lanes) | Serves 2040 traffic volumes Eliminates alignment shifts Estimated corridor crash reduction of 24% Removes 4 trees
Bike Facilities Across Center Bridge | Creates bike connection across bridge
Bike Facilities Along Center Ave | Provides wide outside lane for bicycles
Transit | Removes transit pullout per request Maintains existing transit routes Creates vehicle delays when bus is stopped
Removal of 7th Street Signal | Allows coordination between signals Signal is not warranted
Pedestrians | Removes conflict between bikes and peds Improves ADA compliance
Access | Options to do nothing, relocate or close accesses
Parking | Adds on-street parking
Preliminary Cost | $816,000
Mill & Overlay + 3-Lane Section +
On-Street Parking/Wide Outside Lanes
Notes: Peggy

## Slide 9: Alternative C
Mill & Overlay +
Re-stripe to Existing Lane Configuration
Notes: Peggy

## Slide 10: Alternative C
Alternative Improvements | Issued Addressed/Impacts
Mill & Overlay | Fixes pavement deficiencies
Roadway Section (4-Lanes) | Serves 2040 traffic volumes No corridor crash reduction
Bike Facilities Across Bridge | Creates bike connection across bridge
Bike Facilities Along Center Ave | No Changes
Transit | Maintains existing transit routes
Removal of 7th Street Signal | Allows coordination between signals Signal is not warranted
Pedestrians | No Changes
Access | No Changes
Parking | No Changes
Preliminary Cost | $556,000
Mill & Overlay +
Re-stripe to Existing Lane Configuration
Notes: Peggy

## Slide 11: Alternative D
Mill & Overlay + 3-Lane Section + Roadway Shoulders
Notes: Peggy

## Slide 12: Alternative D
Alternative Improvements | Issued Addressed/Impacts
Mill & Overlay | Fixes pavement deficiencies
Roadway Section (3-Lanes) | Serves 2040 traffic volumes Eliminates alignment shifts Estimated corridor crash reduction of 24% Removes 4 trees
Bike Facilities Across Bridge | Creates bike connection across bridge
Bike Facilities Along Center Ave | No Changes
Transit | Removes transit pullout per request Maintains existing transit routes Creates vehicle delays when bus is stopped
Removal of 7th Street Signal | Allows coordination between signals Signal is not warranted
Pedestrians | Sidewalk improvements Improves ADA compliance
Access | Consideration to Reconstruct Thai Orchid Access in its Current Location
Parking | No Changes
Preliminary Cost | $948,000
Mill & Overlay + 3-Lane Section + Roadway Shoulders
Notes: Peggy

## Slide 13: Additive Alternative 1
4th Street Realignment
Alternative Improvements | Issued Addressed/Impacts
Transit | Maintains existing transit routes
Access | Changes the 4th Street intersection and mall accesses
Preliminary Cost | $774,000
Notes: Peggy

## Slide 14: Public Education: Road Diet Facts & Myth Busters
Notes: Road Diet Info – All Peggy’s slides
Jon add photo of Center Avenue as a 3-lane

## Slide 30: Existing Traffic Operations Analysis (2018)
Notes: Jon

## Slide 31: Forecast Traffic Operations Analysis (2040)
Notes: Jon

## Slide 32: Landscape Opportunities
Notes: Peggy

## Slide 33: Landscape Opportunities
Notes: Peggy

## Slide 34: Landscape Opportunities
Notes: Peggy

## Slide 35: Options Chosen
Option D was the recommended option from staff.
  On street bike lanes favored by bicycle community and City staff.
  Existing surface parking didn’t show the need for on-street parking.
Option B was chosen by Council
  Wide outside lanes are a dedicated bicycle facility that also connect the proposed bike lanes across the bridge to 7th Street. Second favorite of bicycle community.
  Strong support from local business for on-street parking while still providing dedicated bicycle facilities.
  Local business wanted on street parking to allow for future development opportunities in existing surface lots. On-street parking promotes the “downtown feel.”
Notes: Please word smith. Peggy & Jon

## Slide 36: Questions or Comments?
Notes: Add a background photo.